## Slide 1: POWER FLUCTUATIONS
Computer Systems

## Slide 2: Power Fluctuations
Voltage is the force that moves electrons through a circuit
Unsteady voltages are called power fluctuations
Power fluctuations can cause data loss or hardware failure

## Slide 3: Blackout
Total loss of power to an area for a period of time
Can be caused by blown fuse, damaged transformer, downed power line
Protect with Standby generator and/or uninterruptable power supply (UPS) battery

## Slide 4: Brownout
Reduced voltage level below 80% of normal voltage that lasts for a period of time
Computer equipment might try to draw more current and overheat
Use uninterruptable power supply (UPS) to provide backup power for 5-15 minutes

## Slide 5: Power Surges
Sudden increase in voltage
Can be caused by a large user of electricity
shutting down
Can adversely affect systems
Surge protector or voltage regulator

## Slide 6: Power Sag
A sudden decrease in voltage that lasts less than a second
Caused when high powered electrical devices come on line
Can cause computer system to slow down or crash

## Slide 7: Electrical Noise
Electromagnetic Interference (EMI)
Caused by electrical equipment, power lines, storms
Distorts signals
Keep distance from computers
Radio Frequency Interference (RFI)
Occurs in wireless networking when
Radio transmitters and other devices use the same frequency
Data loss or poor performance

## Slide 8: Surge Protector
Protects against sudden surges in voltage
Inexpensive
Acts as a gatekeeper and does not allow excess voltage to pass through to computer
Surge protector will break instead of harm to computer

## Slide 9: Computer Safety
Write a one page essay on what you have learned about Keeping You and Your Computer Safe
Include:
  Electrostatic discharge
  Environmental concerns
  Power Fluctuations